## Slide 1: RnRNPU

## Slide 2: Threat Model
Attack目标
  破坏LLM inference的Integrity（篡改推理流程/影响修改推理结果）
  破坏LLM inference的Confidentiality（读取输入数据/输出结果/模型参数（这个站在用户角度可能不重要？）...）
Attacker能力：控制了整个REE的OS，具有EL1/EL0的所有权限(StrongBox CCS22)
  无法控制REE的EL2
    无法控制第二阶段页表地址翻译，但是可以使用DMA或外设读取（在运行推理时使用TZPC/IOMMU等屏蔽）
  无法控制EL3
    always secure
Attacker攻击面：REE的整个EL0/EL1以及未被屏蔽的外设/DMA
信任边界：整个Secure World+REE EL2
Cryptographic Attack /Side Channel attack /Physical Attack ： Out of scope
  availability： out of scope（可以通过在EL3里用时钟定时preept REE执行来实现availability，但不是这个项目的主要目标）[CCS 23] Jinwen Wang, Yujie Wang, and Ning Zhang, “Secure and Timely GPU Execution in Cyber-physical Systems”, 30th ACM Conference on Computer and Communications Security, 2023.

## Slide 3: System Model
用户面对不可信的环境，选择使用机密LLM推理，目标是能够在Attacker的攻击下保证推理的Integrity&Confidentiality
REE传输加密的参数（句子）到TEE，TEE执行推理后直接输出到屏幕上给用户（独立于REE的UART）或者返回加密后的输出给REE。在执行推理的过程中，TEE使用SoC上的NPU进行加速，同时保证Confidentiality&Integrity。
针对用户最好是能做到Plug and play
  用户的正常推理维持原状
  一旦用户启用confidential模式，整个推理流程就会自动全在TEE中进行，REE不可见（动态屏蔽REE对相关地址/设备的访问）。

## Slide 4: System Design
一次完整的（LLM）机密端侧推理：
  REE Calls Confidential Inference API
  REE Saves address space data and assigns TEE the address space to Run LLM Inference(Wights/Activiations/Results)(此处可能需要REE来load firmware和启动NPU)
  REE sends these parameters to TEE(Address Space to run inference&Encoded User Inputs)
  TEE receives the params, forbids REE’s access, loads and decrypts the encoded Records/Model,Resets NPU then starts to execute
  TEE Run Tokenizer/KVCache/Autoregression/RnR/自己实现的NPU不支持算子
  gets the result
  prints through private UART or Encodes the result then transfers it to REE，then enables REE’s access to corresponding address space and devices/DMA

## Slide 5: System Design
安全性：整个推理流程（Integrity）和结果（Integrity&Confidentiality）都对REE不可见，并且相关的数据REE无法访问（Confidentiality）
Performance：
  尚未明确，可能会降低？
challenge and solution：
  trade off between small TCB and usability
    Record and Replay REE kernel NPU driver execution/interaction
  Memory Constraint
    Enable and Trigger Stage 2 Translation Fault when REE attempts to access Confidential address space(model weights/activiations/results etc) while forbid REE’s DMA/Device request

## Slide 6: System Design
Challenge and solution
  输入参数传递（LLM中的用户输入）
    加密后由REE传递?（StrongBox CCS22 /CODASPY23）（没有见过其它方法）
  Tokenizer/Kvcache/Autoregression
    implement from scratch？
  NPU不支持的算作实现
    implement from scratch？
  Firmware attack(MOLE CCS25)
    How to protect this runtime attack? required to design
Composition of TCB
  Tokenizer: 几百行
    KVCache：几百行
    Autoregression：几百行
    RnR：可能1000左右？
    其它逻辑：NPU不支持的算子实现/模型加载/加密解密/屏蔽REE访问/处理与REE的交互...